## Slide 1: RDMA over Commodity Ethernet at Scale
Chuanxiong Guo, Haitao Wu, Zhong Deng, Gaurav Soni,
Jianxi Ye, Jitendra Padhye, Marina Lipshteyn
ACM SIGCOMM 2016
August 24 2016

## Slide 2: Outline
RDMA/RoCEv2 background
DSCP-based PFC
Safety challenges
  RDMA transport livelock
  PFC deadlock
  PFC pause frame storm
  Slow-receiver symptom
Experiences and lessons learned
Related work
Conclusion

## Slide 3: RDMA/RoCEv2 background
RDMA addresses TCP’s latency and CPU overhead problems
RDMA: Remote Direct Memory Access
  RDMA offloads the transport layer to the NIC
  RDMA needs a lossless network
RoCEv2: RDMA over commodity Ethernet
  DCQCN for connection-level congestion control
  PFC for hop-by-hop flow control
TCP/IP
NIC driver
User
Kernel
Hardware
RDMA transport
IP
Ethernet
RDMA app
DMA
RDMA verbs
TCP/IP
NIC driver
Ethernet
RDMA app
DMA
RDMA verbs
Lossless network
RDMA transport
IP

## Slide 4: Priority-based flow control (PFC)
Hop-by-hop flow control, with eight priorities for HOL blocking mitigation
The priority in data packets is carried in the VLAN tag
PFC pause frame to inform the upstream to stop
PFC pause frame
p1
Egress port
Ingress port
p0
p1
p7
Data packet
p0
p0
p1
p7
XOFF threshold
Data packet
PFC pause frame

## Slide 5: DSCP-based PFC
Issues of VLAN-based PFC
  It breaks PXE boot
  No standard way for carrying VLAN tag in L3 networks
DSCP-based PFC
  DSCP field for carrying the priority value
  No change needed for the PFC pause frame
  Supported by major switch/NIC venders
PFC pause frame
Data packet
TOR Switch
NIC
Trunk mode
No VLAN tag when PXE boot

## Slide 6: Outline
RDMA/RoCEv2 background
DSCP-based PFC
Safety challenges
  RDMA transport livelock
  PFC deadlock
  PFC pause frame storm
  Slow-receiver symptom
Experiences and lessons learned
Related work
Conclusion

## Slide 7: RDMA transport livelock
RDMA Send 0
RDMA Send 1
RDMA Send N+1
NAK N
RDMA Send 0
RDMA Send 1
RDMA Send 2
RDMA Send N+2
Go-back-0
Go-back-N
RDMA Send 0
RDMA Send 1
RDMA Send N+1
NAK N
RDMA Send N
RDMA Send N+1
RDMA Send N+2
RDMA Send N+2
Sender
Receiver
Switch
Pkt drop rate 1/256
Sender
Receiver
Receiver
Sender

## Slide 8: PFC deadlock
Our data centers use Clos network
Packets first travel up then go down
No cyclic buffer dependency for up-down routing -> no deadlock
But we did experience deadlock!
Spine
Leaf
ToR
Podset
Pod
Servers

## Slide 9: PFC deadlock
Preliminaries
  ARP table: IP address to MAC address mapping
  MAC table: MAC address to port mapping
  If MAC entry is missing, packets are flooded to all ports
IP | MAC | TTL
IP0 | MAC0 | 2h
IP1 | MAC1 | 1h
MAC | Port | TTL
MAC0 | Port0 | 10min
MAC1 | - | -
Input
Output
Dst: IP1
ARP table
MAC table

## Slide 10: PFC deadlock
La
Lb
T0
T1
S1
S2
S3
S4
Server
p0
p1
p2
p3
p0
p1
p3
p4
p0
p1
p0
p1
Egress
port
Ingress
port
1
4
3
2
PFC pause frames
p2
S5
Packet drop
Congested port
Dead server
PFC pause frames
Path: {S1, T0, La, T1, S3}
Path: {S1, T0, La, T1, S5}
Path: {S4, T1, Lb, T0, S2}

## Slide 11: PFC deadlock
The PFC deadlock root cause: the interaction between the PFC flow control and the Ethernet packet flooding
Solution: drop the lossless packets if the ARP entry is incomplete
Recommendation: do not flood or multicast for lossless traffic
Call for action: more research on deadlocks

## Slide 12: NIC PFC pause frame storm
A malfunctioning NIC may block the whole network
PFC pause frame storms caused several incidents
Solution: watchdogs at both NIC and switch sides to stop the storm
ToRs
Leaf layer
Spine layer
servers
0
1
2
3
4
5
6
7
Malfunctioning NIC
Podset 0
Podset 1

## Slide 13: The slow-receiver symptom
ToR to NIC is 40Gb/s, NIC to server is 64Gb/s
But NICs may generate large number of PFC pause frames
Root cause: NIC is resource constrained
Mitigation
  Large page size for the MTT (memory translation table) entry
  Dynamic buffer sharing at the ToR
CPU
DRAM
ToR
QSFP
40Gb/s
PCIe
Gen3 8x8 64Gb/s
MTT
WQEs
QPC
NIC
Server
Pause frames

## Slide 14: Outline
RDMA/RoCEv2 background
DSCP-based PFC
Safety challenges
  RDMA transport livelock
  PFC deadlock
  PFC pause frame storm
  Slow-receiver symptom
Experiences and lessons learned
Related work
Conclusion

## Slide 15: Latency reduction
RoCEv2 deployed in Bing world-wide for one and half years
Significant latency reduction
Incast problem solved as no packet drops

## Slide 16: RDMA throughput
Using two podsets each with 500+ servers
5Tb/s capacity between the two podsets
Achieved 3Tb/s inter-podset throughput
Bottlenecked by ECMP routing
Close to 0 CPU overhead

## Slide 17: Latency and throughput tradeoff
L0
T0
L1
T1
L1
L1
S0,0
S0,23
S1,0
S1,23
RDMA latencies increase as data shuffling started
Low latency vs high throughput
us
Before data shuffling
During data shuffling

## Slide 18: Lessons learned
Deadlock, livelock, PFC pause frames propagation and storm did happen
Be prepared for the unexpected
  Configuration management, latency/availability, PFC pause frame, RDMA traffic monitoring
NICs are the key to make RoCEv2 work
Loss vs lossless: Is lossless needed?

## Slide 19: Related work
Infiniband
iWarp
Deadlock in lossless networks
TCP perf tuning vs. RDMA

## Slide 20: Conclusion
RoCEv2 has been running safely in Microsoft data centers for one and half years
  DSCP-based PFC which scales RoCEv2 from L2 to L3
  Various safety issues/bugs (livelock, deadlock, PFC pause storm, PFC pause propagation) can all be addressed
Future work
  RDMA for inter-DC communications
  Understanding of deadlocks in data centers
  Lossless, low-latency and high-throughput networking
  Applications adoption